## Slide 1
Mass Spectrometry
Proteomics
质谱蛋白质组学技术
Principles, Technologies & Applications
Bottom-Up Proteomics — From Sample to Differential Abundance
Technical Background Review · 2026

## Slide 2
Core Principles of MS-Based Proteomics
Complete workflow from biological sample to protein identification and quantification
Sample Preparation
Cell Lysis / Reduction
Alkylation / Cleanup
Trypsin Digestion
Enzymatic Cleavage
Peptide Mixture (~100K)
LC-MS/MS Analysis
ESI Ionization / Orbitrap
MS1 → HCD → MS2 Spectra
Data Analysis
Database Search (FDR<1%)
Protein ID & Quantification
Electrospray Ionization (ESI)
High-voltage electric field generates charged droplets from liquid sample. Solvent evaporation produces multiply-charged gas-phase ions, enabling analysis of large biomolecules including intact proteins and peptide mixtures.
Standard interface for LC-MS coupling
Soft ionization preserves labile PTMs
Orbitrap Mass Analyzer
Ions orbit around a central electrode; their axial oscillation frequencies are detected via Fourier transform. Resolution exceeds 240,000 (FWHM) with mass accuracy below 1 ppm — the gold standard for shotgun proteomics.
Resolution >240K @ m/z 200
Mass accuracy <1 ppm (external calibration)
Acquisition Strategies
DDA selects top-N precursors for fragmentation by abundance. DIA fragments all precursors across fixed m/z windows, achieving >90% inter-run reproducibility versus DDA's ~60%. DIA-NN and Spectronaut enable library-free analysis.
DDA: Deep but stochastic
DIA: Reproducible & comprehensive
>240K
Resolution (FWHM)
<1 ppm
Mass Accuracy
10,000+
Proteins Identified
DDA/DIA
Dual-Mode Strategy
02 — Core Principles

## Slide 3
Key Technologies: DDA vs DIA
Literature-Based Comparison of Data Acquisition Strategies in Bottom-Up Proteomics
DDA — Data-Dependent Acquisition
Principle
MS1 full scan selects top-N most abundant precursor ions for sequential isolation and MS/MS fragmentation. Resulting spectra are matched against protein sequence databases (e.g., UniProt) to identify peptides at FDR < 1%.
Key Advantages
Mature ecosystem: MaxQuant, Proteome Discoverer, Mascot
Deep proteome coverage in discovery mode
Well-established statistical frameworks for differential analysis
Key Literature
Aebersold & Mann, 2003, Nature — Defined the shotgun proteomics framework
Cox & Mann, 2008, Nat. Biotechnol. — MaxQuant: high-resolution quantitative proteomics
DIA — Data-Independent Acquisition
Principle
MS1 scan followed by systematic fragmentation of all precursors within fixed m/z isolation windows across the full mass range. All fragment ions are recorded without bias — creating a complete digital record of every detectable peptide.
Key Advantages
>90% inter-run reproducibility (vs ~60% for DDA)
Quantification CV typically <10% for most proteins
Library-free analysis: DIA-NN, Spectronaut directDIA
Key Literature
Gillet et al., 2012, MCP — SWATH-MS: targeted data extraction from DIA spectra
Demichev et al., 2020, Nat. Methods — DIA-NN: deep learning for proteome coverage
Emerging Frontiers
Ion Mobility Spectrometry (timsTOF/FAIMS): CCS-based 4th dimension separation enables diaPASEF for ultra-deep coverage (Meier et al., 2018, Nat. Methods)
Single-Cell Proteomics: SCoPE2 multiplexing, N2 carrier proteome, TMT-based quantification — pushing sensitivity to single-cell resolution (Slavov, 2020, Science)

## Slide 4
Technology Platforms & Future Outlook
Instrument Capability Matrix and Proteomics Technology Evolution
Orbitrap Astral
Thermo Fisher Scientific
Resolution: >240K (FWHM) @ m/z 200
Scan Speed: >200 Hz (Astral detector)
Mass Accuracy: <1 ppm (external cal.)
Ideal for: Deep proteome / TMT multiplexing
timsTOF Ultra
Bruker Daltonics
CCS Dimension: Ion mobility (TIMS)
Scan Speed: >120 Hz
diaPASEF: 4D proteomics workflow
Ideal for: Single-cell / high-sensitivity DIA
ZenoTOF 7600+
SCIEX
Sensitivity: Zeno trap enhancement
SWATH DIA: Mature, robust ecosystem
Throughput: Optimized for large cohorts
Ideal for: Clinical / population proteomics
Technology Evolution Timeline
2003
Shotgun Proteomics
2012
SWATH-MS / DIA
2018
diaPASEF / 4D
2020
DIA-NN / AI Analysis
2024+
Single-Cell Proteomics
Future
Core Trend
The field is transitioning from DDA to DIA, integrating ion mobility as a 4th dimension, and embracing AI-driven data analysis. Single-cell proteomics and large clinical cohort studies represent the two most critical application frontiers.